## Slide 1: Motherboard

## Slide 2
A motherboard is the most complicated component in a computer. When you put together a computer from parts, generally you start with deciding on which processor and motherboard you will use.
Everything else follows those decisions.

## Slide 3
If you were shopping for a motherboard for a gaming system, you’d have to compare many features among numerous boards.

## Slide 4: Features of motherboard
Generally, you’d need to pay attention to form factor, processor sockets, chipsets, buses and number of bus slots, and other connectors, slots, and ports.

## Slide 5: Motherboard form factor
When you put together a new system, or replace components in an existing system, the motherboard, power supply, and case must all be compatible.
The standards that describe the size, shape, and major features of these components so that they work together are called form factors.

## Slide 6
motherboard form factor determines the size of the board and its features that make it compatible with power supplies, cases, processors, and expansion cards.
The size is also referred to as form factor. Form factor shows the type of board,power supply, number of ports

## Slide 7
When you are deciding which form factor to use, the motherboard drives the decision because it determines what the system can do.
After you’ve decided to use a certain form factor for the motherboard, you must use the same form factor for the case and power supply.
Using a matching form factor for the motherboard, power supply, and case assures you that:

## Slide 8
The motherboard fits in the case.
The power supply cords to the motherboard provide the correct voltage, and the connectors match the connections on the board.
The holes in the motherboard align with the holes in the case for anchoring the board to the case.
Holes in the case align with ports coming off the motherboard.
For some form factors, wires for switches and lights on the front of the case match up with connections on the motherboard.
The holes in the power supply align with holes in the case for anchoring the power supply to the case.

## Slide 9: TYPES OF FORM FACTOR
When selecting a computer case, motherboard, and power supply, choose a design that fits its intended use.

## Slide 10
ATX FORM FACTOR ATX (Advanced Technology Extended) is the most commonly used form factor today.
It is an open, nonproprietary industry specification originally developed by Intel in 1995, and has undergone several revisions since then.
The CPU and memory slots sit beside expansion slots so that full-length expansion cards don’t bump into the CPU or memory modules.

## Slide 11
The original ATX form factor had case fans blowing air into the case but early revisions to the form factor had fans blowing air out of the case.
Blowing air out of the case does a better job of keeping the system cool

## Slide 12
The first ATX power supplies and motherboards used a single power connector called the P1 connector that had 20 pins
Another feature of an ATX motherboard is a soft switch, sometimes called the soft power feature. If an operating system supports the feature, it can turn off the power to a system after the shutdown procedure is done.

## Slide 13
MICROATX FORM FACTOR
The MicroATX form factor is a major variation of ATX and addresses some technologies that have emerged since the original development of ATX.
MicroATX reduces the total cost of a system by reducing the number of expansion slots on the motherboard, reducing the power supplied to the board, and allowing for a smaller case size.
A MicroATX motherboard will fit into a case that follows the ATX 2.1 or higher standard.
A variation of the MicroATX is the Mini-ITX.
This form factor is smaller than the MicroATX and designed for small systems such as a home theatre system.

## Slide 14
FLEXATX FORM FACTOR
FlexATX is a variation of MicroATX. It allows for maximum flexibility (giving it the name FlexATX), and therefore can be a good choice for custom systems.
A FlexATX motherboard can be up to 9" x 7.5".
The motherboard costs less, has fewer features, and is smaller than a MicroATX board.
FlexATX is commonly used in slimline and all-in-one cases, but can fit into any FlexATX, MicroATX, or ATX case that follows the ATX 2.03 or higher standard.

## Slide 15
BTX FORM FACTOR
The BTX (Balanced Technology Extended) form factor was designed by Intel in 2003 for flexibility and can be used by everything from large tower systems to those ultrasmall systems that sit under a monitor.
BTX was designed to take full advantage of serial ATA, USB 2.0, and PCI Express technologies.
The BTX form factor design focuses on reducing heat with better airflow and improved fans and coolers. It also gives better structural support for the motherboard than does ATX.

## Slide 16
BTX motherboards use a 24-pin power connector that has the same pinout arrangement as the ATX 24-pin P1 connector.
The BTX form factor can also use one or more auxiliary power connectors for the processor, fans, and lighting inside the case (for really cool-looking systems). Because the 24-pin connectors are the same, a BTX motherboard can use an ATX power supply

## Slide 17
NLX FORM FACTOR
The NLX (New Low-profile Extended) form factor for low-end personal computer motherboards was developed by Intel in 1998 to improve on an older and similar form factor, called the LPX form factor.
In these systems, the motherboard has only one expansion slot, in which a riser card (also called a bus riser, daughter card, or daughter board), is mounted.
Expansion cards are mounted on the riser card, and the card also contains connectors for the floppy and hard drives.

## Slide 18
The riser card on an NLX motherboard is on the edge of the board, which differs from the LPX motherboard that had the riser card near the center of the board.
The NLX standard applies only to motherboards; NLX motherboards are designed to use ATX power supplies.

## Slide 19: Processor socket
Another important feature of a motherboard is the processor socket.
This socket and the chipset determine which processors a board can support.
A socket will hold either an Intel or AMD processor.
Some older processors were installed on the motherboard in a long narrow slot, but all processors sold today use sockets.

## Slide 20
Earlier Pentiums used a pin grid array (PGA) socket, with pins aligned in uniform rows around the socket.
Later sockets used a staggered pin grid array (SPGA), with pins staggered over the socket to squeeze more pins into a small space.
Small pins can easily be bent as the processor is installed in the socket.
Later Intel sockets use a land grid array (LGA) that uses lands rather than pins.

## Slide 21
The latest Intel socket is the LGA1366 socket.
It’s called a land grid array socket, but the lands in the socket are actually more like pins that connect with lands on the bottom of the processor.

## Slide 22
PGA, SPGA, and LGA sockets are all square or nearly square.
So that even force is applied when inserting the processor in the socket, all current processor sockets have a lever on the side of the socket.
These sockets are called zero insertion force (ZIF) sockets, and this lever is used to lift the processor up and out of the socket.
Push the lever down and the processor moves into its pin or land connectors with equal force over the entire housing.

## Slide 23
However, know that processors generally should not be removed or replaced repeatedly because this can damage the delicate pins or socket holes.
AMD has chosen to use the PGA socket architecture for its desktop processors.
(Some of AMD’s server processors use Socket F, which is an LGA socket.)

## Slide 24: Chipset
chipset is a set of chips on the motherboard that collectively controls the memory, buses on the motherboard, and some peripherals.
A few motherboard manufacturers, such as Intel and AMD, make their own chipsets.
But other motherboard manufacturers use chipsets made by another manufacturer.

## Slide 25
The major chipset manufacturers are Intel (www.intel.com), AMD (www.amd.com), NVIDIA (www.nvidia.com), and SiS (www.sis.com), in that order

## Slide 26: more popular chipsets are listed here:
High-performance chipsets. The X58 chipset supports the Intel LGA1366 socket, the Core i7 processors, and PCI Express Version 2.
It can also support either SLI or CrossFire technologies.
(SLI and CrossFire are two competing technologies that allow for multiple video cards installed in one system.)

## Slide 27
The X58 chipset does not control memory because the memory controller is embedded in the Core i7 processor.
The 975X Express chipset supports the Pentium Extreme Edition processor, multiple video cards, and up to 8 GB of memory.

## Slide 28
Mainstream desktop chipsets.
The P45, P43, P35, G45, and G31 chipsets support Core 2 Quad and Core 2 Duo Intel processors.
P45, P43, and G45 can support up to 16 GB of DDR3 or DDR2 memory.
The P35 chipset supports up to 8 GB of DDR3 or DDR2 memory.

## Slide 29
It also supports the Core 2 Extreme processor. The G31 chipset supports up to 4 GB of DDR2 memory.
The Q45 chipset uses DDR3 or DDR2 memory and supports the Core 2 Duo and Core 2 Quad processors.
All these chipsets use socket LGA775.

## Slide 30
Value desktops. The 910GL, 845E, 845G, and 865G chipsets support the Pentium 4, Celeron, and Celeron D processors in low-end systems.
The 910GL chipset uses the LGA775 socket. The 845E, 845G, and 865G chipsets use the 478PGA socket.
All these chipsets use DDR memory.

## Slide 31
Older value desktops. The 845 and 845GL chipsets support the Pentium 4 or Celeron processors in a low-end system using the 478PGA socket.
They support up to 2 GB of DDR memory.

## Slide 32
AMD purchased ATI Technologies, a maker of chipsets and graphics processors (called a graphics processor unit or GPU), in 2006, which increased AMD chipset and GPU offerings.
Significant chipsets by AMD include the following:

## Slide 33
The AMD 7-series (AMD 790FX, 790X, 790GX, 780, and 770) chipsets are designed with the gamer, hobbyist, and multimedia enthusiast in mind. They focus on good graphics capabilities and support overclocking.

## Slide 34
The AMD 580X Crossfire chipset supports ATI CrossFire.
The AMD 780V chipset is designed for business needs.
The AMD 740G and 690 chipsets are designed for low-end, inexpensive systems.

## Slide 35
Chipsets generate heat, but not as much heat as a processor generates.
Some chipsets today have a heat sink installed on top that is appropriate to keep the chipset cool.
These heat sinks are considered part of the motherboard and you should never have to replace or install one.

## Slide 36
However, some motherboards, such as the Intel DX58SO board, have an optional small fan that you can install on top of the North Bridge chipset to help keep it cool.

## Slide 37: Buses and Expansion Slots
As cities grow, so do their transportation systems.
Small villages have only simple, two lane roads, but large cities have one-way streets, four-lane roads, and major freeways, each with their own set of traffic laws, including minimum and maximum speeds, access methods, and protocols.
As microcomputer systems have evolved, so too have their “transportation” systems

## Slide 38
The earliest PC had only a single simple bus. Today’s PCs have four or five buses, each with different speeds, access methods, and protocols.
As you have seen in previous chapters, backward compatibility dictates that older buses be supported on a motherboard, even when faster, better buses exist.
All this makes for a maze of buses on a motherboard.

## Slide 39
Look on the bottom of the motherboard, and you see a maze of circuits that make up a bus.
These embedded wires carry four kinds of cargo:

## Slide 40
Electrical power. Chips on the motherboard require power to function. These chips tap into a bus’s power lines and draw what they need.
Control signals. Some wires on a bus carry control signals that coordinate all the activity.

## Slide 41
Memory addresses. Components pass memory addresses to one another, telling each other where to access data or instructions. The number of wires that make up the memory address lines of the bus determines how many bits can be used for a memory address. The number of wires thus limits the amount of memory the bus can address.

## Slide 42
Data. Data passes over a bus in a group of wires, just as memory addresses do. The number of lines in the bus used to pass data determines how much data can be passed in parallel at one time. The number of lines depends on the type of processor and determines the number of bits in the data path. (Remember that a data path is the part of the bus on which the data is placed; it can be 8, 16, 32, 64, or more bits wide.)

## Slide 43: THE PCI BUSES
PCI (Peripheral Component Interconnect) buses have been improved several times; there are currently three major categories and within each category, several variations of PCI.
In the following sections, we discuss each category in turn.

## Slide 44: ON-BOARD PORTS AND CONNECTORS
In addition to expansion slots, a motherboard might also have several on-board ports and internal connectors.
Ports coming directly off the motherboard are called on-board ports or integrated components.

## Slide 45
Almost all motherboards have two or more USB ports and sound ports.
Boards might also offer a network port, modem port, FireWire (IEEE 1394) port, video port, keyboard port, mouse port, parallel port, serial port, one or more eSATA ports (for external SATA hard drives), and a port for a wireless antenna

## Slide 46: HARDWARE CONFIGURATION
Settings on the motherboard are used to enable or disable a connector or port, set the frequency of the CPU, system bus, or other buses, control security features, and control what happens when the PC first boots.
In the past, configuring these and other motherboard settings was done in three different ways: DIP switches, jumpers, and CMOS RAM.

## Slide 47
Storing configuration information by physically setting DIP switches or jumpers on the motherboard or peripheral devices was extremely inconvenient, because it often required us to open the computer case to make a change.
A more convenient method is to hold configuration information in CMOS RAM, and today’s computers store almost all configuration data there.
A program in BIOS, called BIOS setup or CMOS setup, can easily make changes to the setup values stored in CMOS RAM.

## Slide 48: SETUP DATA STORED BY DIP SWITCHES
Some older motherboards and expansion cards store setup data using a dual inline package (DIP) switch.
A DIP switch has an ON position and an OFF position. ON represents binary 1 and OFF represents binary 0.
If you add or remove equipment, you can communicate that to the computer by changing a DIP switch setting.
When you change a DIP switch setting, use a pointed instrument such as a ballpoint pen to push the switch.
Don’t use a graphite pencil because graphite conducts electricity. In addition, pieces of graphite dropped into the switch can damage it.

## Slide 49: SETUP DATA STORED BY JUMPERS
Older motherboards can also retain setup or installation information in different settings of jumpers on the board.
Jumpers are considered open or closed based on whether a jumper cover is present on two small posts or metal pins that stick up off the motherboard.
On these older boards, a group of jumpers might be used to tell the system at what speed the CPU is running, or to turn a power-saving feature on or off

## Slide 50
Most motherboards today allow you to set a supervisor password or user password to control access to the system. For example, you can set two passwords in BIOS setup: one to control access to BIOS setup (supervisor password) and the other to lock access to the computer (user password).
If both passwords are forgotten, you cannot use the computer

## Slide 51
However, jumpers can be set to clear both passwords. Also, BIOS firmware might need updating to solve a problem with the motherboard or to use a new motherboard feature.
If updating BIOS fails, jumpers can be set to undo the update.
How to set and clear passwords, update BIOS

## Slide 52: SETUP DATA STORED IN CMOS RAM
Computers today store most configuration information in CMOS RAM, also called the realtime clock/non-volatile RAM (RTC/NVRAM) chip, which retains the data even when the computer is turned off.
Motherboard manuals should contain a list of all BIOS settings (also called CMOS settings), an explanation of their meanings, and their recommended values.

## Slide 53
When you purchase a motherboard or a computer, be sure the manual is included as a printed booklet or on CD.
If you don’t have the manual, you can sometimes go to the motherboard manufacturer’s Web site and download the information you need to understand the specific BIOS settings of your computer.

## Slide 54
Battery Power to CMOS RAM
A small trickle of electricity from a nearby lithium coin-cell battery enables CMOS RAM to hold configuration data, even while the main power to the computer is off.
If the CMOS battery is disconnected or fails, setup information is lost.
An indication that the battery is getting weak is that the system date and time are incorrect after power has been disconnected to the PC.